CSS Reference Card
Mapping of XForms Pseudo Classes to Chiba Classes
Xforms CSS	Chiba CSS classes	Description
:enabled	xfEnabled	Selects a control that is relevant
:disabled	xfDisabled	Selects a control that is not relevant
:required	xfRequired	Selects any core form control bound to a node with the model item property required evaluating to true
:optional	xfOptional	Selects any core form control bound to a node with the model item property required evaluating to false
:valid	xfValid	Selects any core form control bound to a node that is currently valid
:invalid	xfInvalid	Selects any core form control bound to a node that is currently invalid
:read-only	xfReadOnly	Selects any core form control bound to a node with the model item property readonly evaluating to true
:read-write	xfReadWrite	Selects any core form control bound to a node with the model item property readonly evaluating to false
:out-of-range	not defined yet in Chiba	Selects any core form control bound to a node that contains a value the form control is not capable of rendering
:in-range	not defined yet in Chiba	Selects any core form control bound to a node that contains a value the form control is capable of rendering
:value-empty	todo: xfValueEmpty	Selects any core form control bound to a node whose content is the empty string
:value-non-empty	todo: xfValueNonEmpty	Selects any core form control bound to a node whose content is not the empty string

Mapping of XForms Pseudo Elements to Chiba Classes
Xforms CSS	Chiba CSS classes	Description from XForms 1.1 CR
::value	xfValue	Represents the "active" area of a form control excluding the label; this corresponds in HTML to input and other form control elements. This pseudo-element is a child of the form control element, and appears immediately after the required label element.
::repeat-item	xfRepeatItem	Represents a single item from a repeating sequence. Its position is as a parent to all the elements in a single repeating item. Each ::repeat-item is associated with a particular instance data node, and is affected by the model item properties (e.g. 'relevant') found there, as the related style properties will cascade to the child elements.
::repeat-index	xfRepeatIndex	Selects any core form control bound to a node with the model item property required evaluating to trueRepresents the current item of a repeating sequence. Its position is as a parent of all the elements in the index repeating item (and as a child to the ::repeat-item pseudo-element), thus any style declarations applying to this pseudo-element override those on the parent ::repeat-item.

Chiba Classes applied to XForms Elements
XForms Element	CSS classes	Description
Container
group	xfGroup	matches an Element that represents a XForms group element
repeat	xfRepeat	matches an Element that represents a XForms repeat element
switch	xfSwitch	matches an Element that represents a XForms switch element
case	xfCase	matches an Element that represents a XForms case element
Controls
input	xfInput	matches an Element that represents a XForms input element
output	xfOutput	matches an Element that represents a XForms output element
range	xfRange	matches an Element that represents a XForms range element
secret	xfSecret	matches an Element that represents a XForms secret element
select	xfSelect	matches an Element that represents a XForms select element
select1	xfSelect1	matches an Element that represents a XForms select1 element
submit	xfSubmit	matches an Element that represents a XForms submit element
textarea	xfTextarea	matches an Element that represents a XForms textarea element
upload	xfUpload	matches an Element that represents a XForms upload element
Helper
alert	xfAlert	matches an Element that represents a XForms alert element
label	xfLabel	matches an Element that represents a XForms label element
hint	xfHint	matches an Element that represents a XForms hint element
help	xfHelp	matches an Element that represents a XForms help element
other
item	xfSelectorItem	matches an Element that represents a XForms item element
any control	xfRequiredSymbol	matches an Element that is bound to a required Node

For following XForms Attributes Chiba CSS Classes get generated with following pattern / Token Description Example / 'xf' literal Prefix xf / [$upperCaseName] local name of XForms Element first letter uppercased Group / [$appearance] value of XForms @appearance Attribute first letter uppercased Minimal / [$datatype] Schema datatype of bound Node first letter uppercased Integer / [$incremental] value of XForms @incremental Attribute first letter uppercased Incremental
Attribute/property	Matcher Creation Rule	Examples
appearance	'xf'[l$appearance][$upperCaseName]	xfFullGroup, xfMinimalSelect
type	'xsd'[$datatype]	xsdString, xsdAnyURI
incremental	'xf'[$incremental]	xfIncremental

<xf:repeat appearance=”compact”>
each <td>	col1, col2, col3 ...